Safe Work Method Statement

Job:.	Handling hire trailers and house floats		  Client:  Billy Thorpe

Location:	415 Johns Street Bayswater……..

Date: . 21/07/2007				Project Duration:  27 / 07 /  2007	to	29 / 07 /  2007

Principle Contractor:

Prepared By:   John

Consultation with: 	 Phillip, & 	Trish

| Tools and Equipment required | Personal Protective Equipment | Skills and Competencies Required |
| --- | --- | --- |
| Jockey wheel | Gloves High Visibility Vest (Day/Night) | Manual Handling |

SAFE WORK METHOD STATEMENT

Job:  Handling hire trailers and house floats           Client:  ......................................................................................

| STEP BY STEP WORK ACTIVITY | POTENTIAL HAZARD/RISK What are the potential hazards that could cause a safety incident or injury? | CONTROL MEASURES Elimination – eliminate the work practice, plant and/or equipment responsible for the hazard. Substitution – substitute the work practice, plant and/or equipment for a safer alternative. Engineering control – redesign the work practice, use of materials, plant or equipment to attain a safer alternative. Administrative Control – change the procedures to reduce exposure (job rotation, training etc) Protective Equipment for Personnel – select appropriate equipment/apparel to reduce risk/exposure. | Name of responsible person to action |
| --- | --- | --- | --- |
| 1. Clear work area. | Struck by vehicle Slips trips and falls Extreme weather conditions | Observe vehicle movement on the forecourt around the trailer/horse float parking area. Ensure there is no evidence of spills in the area Step carefully over any curbs or uneven surfaces Relocate objects or vehicles that could impede movement of the trailer or horse float. |  |
| 2. Prepare the trailer or horse float. | Manual force required to lift the drawbar. Force to reposition the trailer or horse float to align it with the vehicle Dropping or rolling the drawbar/jockey wheel on the foot. Jamming fingers in the coupling or safety chains on the drawbar. | Wear enclosed footwear at all times Use a jockey wheel to raise / lower drawbar Use chocks behind the wheels to eliminate the trailer or horse float rolling backwards Reverse the vehicle to the drawbar rather than manually pull the trailer or float to the car Wear gloves to protect the fingers from grease and damage Regularly lubricate the couplings to ensure minimal force to operate |  |
| 3. Attaching to vehicle | Entrapment of fingers Manual force to position coupling onto tow bar Rolling the jockey wheel onto the feet | Use the jockey wheel to elevate the drawbar and to lower it onto the tow bar Seek assistance if fine movement of the trailer or horse float is required to accurately position it for coupling Use a “straddle stance” lifting technique at the lifting point to balance the body and keep the feet away from the jockey wheel |  |
| 4. Reversing the trailer or horse float | Struck by vehicle Damage to property | Before reversing ensure a “spotter” is located with clear view behind the horse float or trailer. Clear the parking area of obstructions Check overhead clearance for tall trailer canopies and horse floats |  |